## Slide 1: Smart Fan
By Samolă Ciprian

## Slide 3: I’m joking… This is my fan

## Slide 4: Functionalities
Three speed levels
Controlled by a remote
Stops when someone may be harmed

## Slide 5: Componemts

## Slide 6
3-6v DC motor with fan blade
L293D
Used for controlling the motor (change speed, direction)
It is unsafe to connect the motor directly to development board

## Slide 7
IR Receiver
- Detects IR light only at specific frequency (38 kHz)
Remote

## Slide 8
Ultrasonic Sensor
Can measure 2 -> 400 cm
Precision: 3mm
Sends 40kHz signals, detect whether there is a signal back
Buzzer
Vibrates at some specific frequency => creates a sound
actuator

## Slide 9: One problem…
The DC motor adds noise in the circuit. When it is ON, the IR Receiver doesn’t get signals anymore…
The solution
I added a capacitor to filter out the noise

## Slide 10
The code
State diagram (sort of)

## Slide 11
Further improvements
7 segment display that displays the speed level
An integrated temperature sensor
Phone control

## Slide 12: Thank you for your kindly attention